## Slide 1: TABLETS
Dr. Dipti Gohil
Associate Professor
Subject- BP 502 Industrial Pharmacy-I
Department of Pharmacy, SVDU

## Slide 2: Granulation
A size enlargement process which converts small particles into physically stronger & larger agglomerates.
Granulation method can be broadly classified into three types:
Wet granulation
Dry granulation
Direct compression

## Slide 3: Ideal characteristics of granules
spherical shape,
smaller particle size distribution with sufficient fines to fill
void spaces between granules,
adequate moisture (between 1-2%),
good flow,
good compressibility and
sufficient hardness.

## Slide 4
The effectiveness of granulation depends on the following properties
i) Particle size of the drug and Excipients
ii) Type of binder (strong or weak)
iii) Volume of binder (less or more)
iv) Wet massing time (less or more)
v) Amount of shear applied
vi) Drying rate (Hydrate formation and polymorphism)

## Slide 5: Wet granulation
The most widely used process of agglomeration (granulation) in pharmaceutical industry is wet granulation.
Wet granulation process simply involves wet massing of the powder blend with a granulating liquid, wet sizing and drying.

## Slide 6: Limitation of Wet Granulation
i) Cost: It is an expensive process because of labor, time, equipment, energy and space requirements.
ii) Loss of material during various stages of processing
iii) Stability may be major concern for Moisture sensitive or thermo labile drugs
iv) Multiple processing steps add complexity and make validation and control difficult
v) An inherent limitation of wet granulation is that any incompatibility between formulation components is aggravated.

## Slide 7: Dry Granulation
In dry granulation process the powder mixture is compressed without the use of heat and solvent.
It is the least desirable of all methods of granulation. The two basic procedures are to form a compact of material by compression and then to mill the compact to obtain a granules.

## Slide 8
Two methods are used for dry granulation.
The more widely used method is slugging, where the powder is precompressed and the resulting tablet or slug are milled to yield the granules.
The other method is to precompress the powder with pressure rolls using a machine such as Chilosonator.

## Slide 9: Advantages of dry granulation
Less equipments and space.
It eliminates the need for binder solution, heavy mixing equipment and the costly and time consuming drying step required for wet granulation.
Slugging can be used for advantages in the following situations:
For moisture sensitive material
For heat sensitive material
For improved disintegration since powder particles are not bonded together by a binder

## Slide 10: Disadvantages of dry granulation
It requires a specialized heavy duty tablet press to form slug
ii) It does not permit uniform colour distribution as can be achieved with wet granulation where the dye can be incorporated into binder liquid.
iii) The process tends to create more dust than wet granulation, increasing the potential contamination

## Slide 11: Important steps involved in the dry granulation
Milling of drugs and excipients
Mixing of milled powders
Compression into large, hard tablets to make slug
# Screening of slugs
Mixing with lubricant and disintegrating agent
Tablet compression

## Slide 12: Direct Compression
In this method only blending & compression is involved.
Advantages:
Increased output,
Reduced costs,
Less machinery,
Improved drug stability,
Faster dissolution of drugs,
Less wear & tear of punches,
Simplified validation.

## Slide 13: Disadvantages:
Segregation : problems arises in wt. variation & content uniformity.
Cost: as the directly compressible excipients are costly the cost of tablet is more
Low dilution potential: as the active material is only 30-40% as the requirement of excipient, it is difficulty to the patients to swallow
Not useful for drugs having poor flow properties or low bulk density

## Slide 14: Reasons for Granulation
To prevent segregation of the constituents of the powder mix.
Segregation (or demixing) is due primarily to differences in the size or density of the components of the mix.
The smaller and/or denser particles concentrating at the base of a container
The larger and/or less dense ones above them.
An ideal granulation will contain all the constituents of the mix in the correct proportion in each granule and segregation of the ingredients will not occur.

## Slide 15
To improve the flow properties of the mix
Many powders, because of their small size, irregular shape or surface characteristics, are cohesive and do not flow well.
Poor flow will often result in a wide weight variation within the final product owing to variable fill of tablet dies etc.

## Slide 16
Some powders are difficult to compact even if a readily compactable adhesive is included in the mix and some are compacted easily.
Solute migration occurring during the post granulation drying stage results in a binder-rich outer layer to the granules.
This in turn leads to direct binder–binder bonding, which assists the consolidation of weakly bonding materials.

## Slide 17: Dry granulators
Dry granulation converts primary powder particles into granules using the application of pressure without the intermediate use of a liquid.
It therefore avoids heat-temperature combinations that might cause degradation of the product.
The method is also know as slugging

## Slide 18
Two pieces of equipment are necessary for dry granulation:
First, a machine for compressing the dry powders into compacts or flakes, and
Secondly a mill for breaking up these intermediate products into granules.

## Slide 19
Sluggers:
Dry powders can be compressed using a conventional tablet machine or, more usually, a large heavy duty rotary press can be used.
This process is often known as 'slugging',
A hammer mill is suitable for breaking the compacts.

## Slide 20
Roller compactors:
Powder mix being squeezed between two rollers to form a compressed sheet
The sheet normally is weak and brittle and breaks immediately into flakes.
These flakes need gentler treatment to break them into granules, and this can usually be achieved by screening alone.

## Slide 21
Fig. Schematic diagram of a Chilsonator Roller Compactor in a granulation production system

## Slide 22
Chilsonator roller compactor :
Roller compactor ,utilizes two rollers that revolve towards each other which produce a known pressure on powdered materials that flows between the roller.
Powdered material is feed between the rollers by screw conveyer system. After passing through the roller, the compact mass is breaked by breaker. The segments are then screened or milled for production of granules.

## Slide 23: 3. Direct compression:
Processing steps are:
Raw material → Weighing → Screening → Mixing → Compression.
Direct compression consists of compressing tablets directly from powdered materials without modifying physical nature of materials.
This method is applicable for crystalline chemicals having good compressible characteristic and flow properties such as: Potassium salt (chlorate, chloride, bromide), Sodium chloride, Ammonium chloride, Methenamine etc.

## Slide 24
If necessary, direct compression vehicles can be used which are having good flow and compressible characteristics.
Commonly used directly compression diluents are:
MCC (Microcrystalline cellulose (Avicel),
Spray dried lactose,
Starch - (Sta Rx 1500,
Embdex, Celutab),
Sugar ( Sugartab, Nutab),
Dicalcium phosphate dihydrate (Di-Tab),
Mannitol for chewable tablet.

## Slide 25
Advantages:
1. Low labour input
2. A dry process
3. Fewest processing steps
Disadvantages:
1. Stratification may occur due to differences in particle size and bulk density which results poor content uniformity.

## Slide 26
2. A large dose drug may cause problem in direct compression. It requires diluents. The tablet becomes large in size which is difficult to swallow and also costly.
3. During handling of dry materials static charge may form which may present uniform distribution of drug.
4. Direct compression diluent may interact with the drug. For example, amine drug with Lactose produce discoloration of tablet.

## Slide 27: Types of Granulators
Mixer | Dryers | Granulator
1.Tumbling mixer (Twin-shell blender) | 1.Tray dryer | 1.Fluid bed spray granulator
2. Double cone mixer | 2. Spray dryer | 2. Double cone mixer dryer processor
3. Planatory mixer | 3. Fluidized bed dryer | 3. Nauta processor
4. Sigma blade mixer |  | 
5. Ribbon mixer |  | 
6. High speed chopper blade mixer |  | 

## Slide 28: MIXER
Twin shell blender: The materials are placed in the V-shaped chamber and rotate on its horizontal axis. Due to tumbling action materials are mixed uniformly.
Fig. Twin shell blender

## Slide 29
Double cone blender: The materials to be mixed are placed inside the conical chamber and rotate along its horizontal axis.
Fig. Double cone blender

## Slide 30
Sigma blade mixer: Sigma type blades are rotates in same direction along horizontal axis. Suitable for powder, semisolid material.
Fig. Sigma“Z”blade mixer

## Slide 31
Ribbon mixer: Two spiral ribbons are fixed on a horizontal shaft, which rotates the ribbon. The bending of the ribbon is such that two ribbons move materials in two opposite direction and promote uniform mixing.
Fig. Ribbon mixer

## Slide 32
Planetary mixer: A set of mixing blade rotates as planet around the mixing bowels.
Fig. Planetary mixer

## Slide 33
High-speed chopper blade mixer: The mixer consists of a bowl mounted in vertical position. A high-speed mixer blade revolves around the bottom of the bowl. The mixer also contains a high-speed chopper blade which functions as lump or agglomerate breaker.
Fig. High-speed chopper blade mixer.

## Slide 34
Fig.High-speed chopper blade mixer. (1) Mixer bowel (2) High-speed mixer blade (3) High-speed chopper blade (4) Pneumatic discharge port. (5) Mixed lid. (6) Exhaust air sleeve. (7) Mixer control panel.

## Slide 35: DRYER
Tray dryer: Also called shelf, cabinet or compartment dryer.
Area of each tray: 4 to 8 sq.ft.
Load thickness: 0.5 –4 inches.
Capacity: 500-2000lb/batch
Fig. 8 Tray dryer

## Slide 36
Spray dryer: Can handle only liquid as solution, Slurries, dispersed as fine droplets into a moving stream of hot gas. The solvent evaporates and dried product collected by gas current-gravity flow collection system.
Fig. Spray dryer

## Slide 37
Fluidized bed dryer: In FBD, the fluidizing air stream is introduced by a fan or blower mounted in at the top of the apparatus.
The air is heated to the required temperature in an air heater and flows upward through the wet materials, which contained in a drying chamber fitted with a wire mesh supported at the bottom
Capacity: 5-200 kg
Drying time: 20 to 40 mins
Type: Batch type

## Slide 38
Fig. Fluidized bed dryer

## Slide 39
GRANULATOR
Fluidized bed spray granulator: The unit is same as fluidized bed dryer. When the unit is used as granulator the dry ingredients are placed in the chamber and fluidized while the granulating liquid is sprayed into the bed causing the particles agglomerate into granules.

## Slide 40
Fig. Fluidized bed spray granulator

## Slide 41
Double cone mixer dryer processor: This is modified double cone blender used to perform operation – mixing, wet massing, agglomeration and drying.
Liquid feed system is through the trunion of the machine and sprayed. Vacuum system is through same or opposite trunion providing a nilon filter. Agitators rotate within the powder mass.

## Slide 42
Nauta Mixer Processor: A screw assembly is mounted in a conical chamber within the screw lifting the powder from bottom to top. The screw assembly orbits around the conical chamber wall to ensure more uniform mixing.
The operation is power mixing with incorporation of the liquid granulating agents, wet massing and drying as hot, dry air is passed through the wet materials.

## Slide 43
Fig. Nauta processor