## Slide 1
PACEMAKER BASICS
By:Yash Rakholiya

## Slide 4: A Pacemaker Must Be Able to Sense and Respond to Cardiac Rhythms
Accurate sensing enables the pacemaker to determine whether or not the heart has created a beat on its own
The pacemaker is usually programmed to respond with a pacing impulse only when the heart fails to produce an intrinsic beat

## Slide 5: General indications for pacemaker
Heart rate is slow, causing hemodynamic compromise Sick sinus syndrome
sinus bradycardia or atrial fibrillation with slow heart rate response (generally < 40bpm)
Heart block
3rd degree
2nd degree type 2 (Mobitz)
Malignant Tachyarrhythmia caused by bradycardia

## Slide 6: Clinical settings for temporary pacemaker
Syncope
Myocardial infarction
Especially inferior
Shock due to bradycardia
Myocarditis
Lyme disease

## Slide 7: Another 3rd degree heart block

## Slide 8: Atrial Fibrillation → Asystole

## Slide 10: Pacemaker Components Combine with
Pulse generator: power source or battery
Leads or wires
Cathode (negative electrode)
Anode (positive electrode)
Body tissue
IPG
Lead
Anode
Cathode
Body Tissue to Form a Complete Circuit

## Slide 11: The Pulse Generator:
Contains a battery that provides the energy for sending electrical impulses to the heart
Houses the circuitry that controls pacemaker operations
Circuitry
Battery

## Slide 12: Leads Are Insulated Wires That:
Deliver electrical impulses from the pulse generator to the heart
Sense cardiac depolarization
Lead

## Slide 13
Flows through the tip electrode (cathode)
Stimulates the heart
Returns through body fluid and tissue to the IPG (anode)
A Unipolar Pacing System Contains a Lead with Only One Electrode Within the Heart; In This System, the Impulse:
Cathode
Anode
-

## Slide 14: A Bipolar Pacing System Contains a Lead with Two Electrodes Within the Heart. In This System, the Impulse:
Anode
Flows through the tip electrode located at the end of the lead wire
Stimulates the heart
Returns to the ring electrode above the lead tip
Cathode

## Slide 16: Advantages and Disadvantages of
Single-Chamber Pacing Systems
Advantages
Implantation of a single lead
Disadvantages
Single ventricular lead does not provide AV synchrony
Single atrial lead does not provide ventricular backup if A-to-V conduction is lost

## Slide 18: Benefits of Dual Chamber Pacing
Provides AV synchrony
Lower incidence of atrial fibrillation
Lower risk of systemic embolism and stroke Lower incidence of new congestive heart failure Lower mortality and higher survival rates

## Slide 19: The Can AKA “Pulse Generator,” “Battery”
Temporary
Single chamber Dual chamber Permanent single chamber

## Slide 20: Schematic of pacemaker system

## Slide 22: Examples
21
VVI
V: Ventricle is the paced chamber
V: Ventricle is the sensed chamber
I: Inhibited response to a sensed signal
Thus, a synchronous generator that paces and senses in the ventricle
Inhibited if a sinus or escape beat occurs Called a “demand” pacer

## Slide 23: Most Pacemakers Perform Four Functions:
Stimulate cardiac depolarization
Sense intrinsic cardiac function
Respond to increased metabolic demand by providing rate responsive pacing
Provide diagnostic information stored by the pacemaker

## Slide 24
10
Capture
Depolarization of atria and/or ventricles in response to a pacing stimulus

## Slide 25: Sensing
11
Ability of device to detect intrinsic cardiac activity
Undersensing: failure to sense Oversensing: too sensitive to activity

## Slide 26
Amplitude
Pulse width
Two Settings Are Used to Ensure Capture:

## Slide 27: Amplitude is the Amount of Voltage
Delivered to the Heart By the Pacemaker
Amplitude reflects the strength or height of the impulse:
The amplitude of the impulse must be large enough to cause depolarization ( i.e., to “capture” the heart)

## Slide 28: Pulse Width Is the Time (Duration)
of the Pacing Pulse
Pulse width is expressed in milliseconds (ms)
The pulse width is just the length of time each pacing pulse is delivered & must be long enough for depolarization to disperse to the surrounding tissue
5 V
0.5 ms
0.25 ms
1.0 ms

## Slide 29: Impedance
The opposition to current flow
In a pacing system, impedance is:
Measured in ohms
Represented by the letter “R” ( for numerical values)
The measurement of the sum of all resistance to the flow of current

## Slide 30: Impedance Changes Affect Pacemaker Function and Battery Longevity
High impedance reading reduces battery current drain and increases longevity
Low impedance reading increases battery current drain and decreases longevity
Impedance reading values range from 300 to 1,500 
– High impedance leads will show impedance reading values greater than 1,500 ohms

## Slide 31: Rate Responsive Pacing
When the need for oxygenated blood increases, the pacemaker ensures that the heart rate increases to provide additional cardiac output
Adjusting Heart Rate to Activity
Normal Heart Rate
Rate Responsive Pacing Fixed-Rate Pacing
Daily Activities

## Slide 34: Sites of insertion for a Temporary pacemakers
Right internal jugular
Left subclavian vein
Right subclavian vein
Either femoral vein (Fluoroscopy required)
Left IJ is possible but very difficult

## Slide 46: Complication of temporary pacemaker insertion
Blood loss/hematoma
Infection
Arrhythmia (especially during insertion)
PVC’s are common
Heart block
Especially in patients with underlying LBBB
Bundle branch block
Pneumothorax (about 1+% when subclavian access used)
Cardiac perforation → Tamponade

## Slide 47: Pneumothorax of Left Lung

## Slide 48: The dials on the Temporary pacemaker
Rate
Determines the lower rate limit of the device
Heart rate should not go lower than the set rate
Output
In milliamps, the amount of ‘juice’ the device outputs with each pacer spike

## Slide 49
Sensitivity
In millivolts, the amount of energy that has to be
detected in order for the device to ‘sense’ a beat.
• Higher millivolts = less sensitive
More likely for the pacemaker to pace at the lower
rate regardless of what the heart does on its own.
• Lower millivolts = more sensitive
More likely to pick up noise, and ‘sense’ a ventricular
beat even though nothing actually happened