## Slide 1: Presented By: Yash Rakholiya

## Slide 2: History
Egas Moniz: Cerebral angiography
1927
1929
Werner Forssmann: Cardiac catheterisation
1940
Andre Cournand and Dickinson Richards: Catheterisation and hemodynamics

## Slide 3: Goals
arteries,
branches,
To visualize coronary collaterals and anomalies.
Precise localization of lesion, side branches, thrombi and areas of calcification
To monitor cardiac hemodynamics.

## Slide 4: Cardiac catheterisation laboratory

## Slide 5: Fluoroscopy machine
The X-ray machine is suspended from the ceiling.
It can be manipulated in multiple angles and views to achieve a desired picture.
The x-ray comes from the bottom of the machine and the image intensifier that transmits the image is above the patient.

## Slide 8: INDICATION
Diagnosis of CAD in clinically suspected pts.
Percutaneous coronary intervention
Coronary anomalies
To exclude stenoses before non-coronary cardiac surgery (valve surgery after 40 yrs of age)
Determine patency of coronary artery bypass grafts
17

## Slide 9: INDICATIONS
acute (e.g.,
In patients with non–ST-segment elevation coronary syndromes with high-risk features ongoing ischemia, heart failure)
In patients with acute ST-segment elevation myocardial infarction (STEMI)
Primary percutaneous intervention (PCI) is usually performed in the same procedure, immediately after the diagnostic procedure

## Slide 10: CONTRAINDICATIONS
Coagulopathy
Decompensate congestive heart failure
Uncontrolled Hypertension
CVA
GI Hemorrhage
Pregnancy
Inability for patient cooperation
Active infection
Renal Failure
Contrast medium allergy
19

## Slide 11: Before the Procedure
After patient is properly identified, the procedure must be explained before consent can be signed
Baseline vital signs will be done.
Blood tests must be done including CBC, RFT, Blood sugar levels, Serology

## Slide 12: Patient Preparation
The area being punctured must be shaved properly-RA, LA, RF
Hair removal done by disposable electric razor and removed by sticky side of cloth tape.
IV access must be taken in left forearm.
IV fluid should be started for hydration.
Ornaments and valuables must be removed prior.

## Slide 13
Pre medication should be given- AVIL and hydrocort.
Antibiotic 1 dose prior to procedure.
Alprazolam for patient in anxiety or pain.
Patient should urinate before the procedure.
Patient should not walk from ICCU to cath lab, he should be taken into either wheel chair or stretcher.

## Slide 14: Sterile Field and Patient
The staff working with the cardiologist must be scrubbed properly and wearing lead aprons, sterile gown, face mask, head cap, sterile gloves and shoe cover.
The patient is made to lie down on the table comfortably.
ECG leads and plethysmography probe should be connected.
IV access should be restarted.

## Slide 15
Right Radial site should be cleaned by Spirit- Betadine- Spirit.
Arm rest must be put and a 500ml NS fluid bottle should be kept over it.
Patient is then instructed to keep wrist on that bottle with proper extension so as radial artery pops out.

## Slide 16
Patient is then covered from neck to toe with sterile plastic sheet followed by drapes with hole at puncture site.
All equipment (radiation shields, image intensifier, equipment used to manipulate machine) must be prepped with sterile covers

## Slide 17: Sterile equipment needed
Procedure tray should include:
-sterile gowns and gloves for scrub tech and doctor
-sterile towels and drapes for procedure
-equipment covers
-gauze
-scalpel, needles, scissors, hemostats
-syringes for heparin/saline flush, lidocaine, and blood draw
-labels with marking pen for any item filled with a solution
-basin for heparin/saline mixture, basin for waste fluids, small cup for lidocaine
-skin prep solution
-high power manifold
-connection tubing

## Slide 18
Syringe 1- 2% lignocaine (5ml),
Syringe 2- 5000 iu heparin
Syringe 3- 200ug NTG.(4ml)
Syringe 4- Dilzem 5mg(1ml)
Syringe 5- flush NS

## Slide 19: Radial access tools

## Slide 20
START PROCEDURE
When doctor and tech are scrubbed and all equipment and supplies are ready, the procedure may begin

## Slide 21: Arterial Puncture
Access is easiest from right side of patient due to aortic bend
Puncture is generally done via the Right radial artery
Alternative sites include the Femoral and
brachial arteries of the arm

## Slide 22: Radial
No need for immobilisation
Lower rate of local vascular complications
Increasingly being used as primary access site
Spasm, loops, failure to get access may require switch to femoral route

## Slide 23: Catherization

## Slide 24: Femoral
Previously most frequently used access site
Ease of access, lesser contrast and radiation exposure, freedom to upgrade to bigger size sheaths
Need for immobilisation, local site complications: main drawbacks

## Slide 25: Femoral

## Slide 26: Access technique

## Slide 27: Access sites (Other)
Brachial
Ulnar
Radial in anatomical snuffbox

## Slide 28: Coronary angiography catheters

## Slide 29: Steps to Insert Sheath
After numbing the radial area, the radial artery is palpated and a needle is inserted in that direction.
When blood comes out of needle, the artery has been accessed.
A small, flexible guidewire is then inserted into the lumen of the needle.
The needle can then be removed but the wire must maintain position.

## Slide 30: Inserting Catheter
After removing the needle, a flexible plastic tube can be placed over the wire and introduced into the artery. This is called a one- way sheath (allows insertion of catheters and wires without blood escaping)
The catheter is then inserted over the guidewire but through the sheet and advanced.
MC Catheter used is TIGER

## Slide 31: Catheter Placement
Movement of catheter is monitored under fluoroscopy with the cardiologist manipulating its movements
The fluoroscopic machine is manipulated by a qualified, scrubbed in, radiologic technologist
When catheter is in place, wire can be removed and contrast administered

## Slide 32: Contrast Media
Contrast media-Low osmolarity, Non-ionic
320-370 mg of iodine/mg, connnected to manifold in airfree system.
Left coronary artery is filled with 6-8 ml, right coronary artery is filled with 3-5 ml usually
35

## Slide 33: Contrast Injection
Left coronary artery: 6-8ml over 2-3 seconds
Right coronary artery: 4-6ml over 2-3 seconds
Should be adequate to fill the coronary artery completely
without streaming
Excessive contrast injection should be avoided
Cine acquisition (@10fps) should continue till contrast clears from the system

## Slide 34: Normal coronaries (LCA)

## Slide 35: Normal coronaries (RCA)

## Slide 43: Angiographic views of the left coronary artery

## Slide 44: Angiographic views of the right coronary artery

## Slide 45: Calcification

## Slide 46: Thrombus

## Slide 47: Tortuousity

## Slide 48: Dissection

## Slide 49
43
Tight stenosis noted involving the mid segment of right coronary artery. Distal branches are normal.
A partially obstructive narrowing noted in the proximal segment of the LAD

## Slide 50: Muscle Bridge

## Slide 51: Possible complications
Femoral : Dissection of femoral / iliac artery or aorta , Haematoma, pseudoaneurysm
Aorta : Damage to aortic intima , Embolus to head and neck vessels, aortic root dissection.
Coronary : Ostial dissection, coronary embolus, arrhythmia due to catheter wedging or contrast medium, spasm due to catheter or contrast medium.
General : Hypotension, left heart failure – contrast overload, Contrast allergy

## Slide 52: Finished Procedure
The procedure is complete when the radiologist or cardiologist has seen all the views and anatomy desired and all pressures recorded.
The catheter can be removed and patient is connected with intra-arterial line for 15 minutes.
Patient then can be shifted back to observation.

## Slide 53
Patient reconnected to monitor via arterial line and observed for anaphylaxis.
After 30 minutes patient can be given something to eat or drink.
Radial sheath can be removed within 15 minutes for normal angiogram and after 3hours of PCI.
Require 15-20 minutes of pressing.

## Slide 54: Femoral Instructions
The patient must lie flat and supine for a minimum of 2 hours to ensure the artery does not reopen.
Sheath can be removed after 5-6 hours.
Need presssing for 30-40 minutes.
Dressing must remain dry,
Patient must lie flat and supine for 12 hours minimum.
Observe for femoral hematoma and RPH

## Slide 55
After the case is over, Cath lab is cleaned properly for any blood stains, new set of trolley is prepared and old material is packed to be sent for autoclaving.
If patient is seropositive, whole material is discarded.

## Slide 56: Coronary artery
Coronary artery is a vasa vasorum that supplies the heart.
Coronary comes from the latin ”Coronarius”
Meaning “Crown”.
4

## Slide 57: Coronary artery
–
The coronary artery arises just superior to the aortic valve and supply the heart
The aortic valve has three cusps #left coronary (LC),
#right coronary (RC) #posterior non-coronary (NC)
cusps.
5

## Slide 58: Right coronary artery
Originates from right coronary sinus of Valsalva
Courses through the right AV groove between the right atrium and right ventricle to the inferior part of the septum
6

## Slide 59: Branches of RCA
7
Right coronary artery
Conus artery
Sinu nodal artery
Marginal artery
Post. Descending IV artery
Conus branch
SINU NODAL BRANCH
AVAVnNooddaallBararntechry-

## Slide 60
Conus branch – 1st branch supplies the RVOT
Sinus node artery – 2nd branch - SA node.(in 40% they originate from LCA)
Acute marginal arteries-Arise at acute angle and runs along the margin of the right ventricle above the diaphragm.
Branch to AV node: PLV
Posterior descending artery : Supply lower part of the ventricular septum & adjacent ventricular walls.
Arises from RCA in 85% of cases.
8

## Slide 61: Area of distribution
1)Right atrium 2)Ventricles
greater part of rt. Ventricle except the area adjoining the anterior IV groove.
a small part of the lt. ventricle adjoining posterior IV groove.
Posterior part of the IV septum.
9

## Slide 62: Left coronary artery
Arises from left coronary cusps
Travels between RVOT anteriorly and left atrium posteriorly.
Almost immediately bifurcate into left anterior descending and left circumflex artery.
Length – 10-15cm
10

## Slide 63: LT CORONARY ARTERY DISTRIBUTION
Left atrium.
Ventricles
Greater part of the left ventricle, except the area adjoining the posterior IV groove.
A small part of the right ventricle adjoining the anterior IV groove.
Anterior part of the IV septum.
LBB and RBB
12

## Slide 64: DOMINANCE
Determined by the arrangement that which artery supply posterior descending artery
The right coronary artery is dominant in 85% cases.
8% cases - - circumflex br of the left coronary artery
7% both rt & lt coronary artery supply posterior IVseptum & inferior surface of the left ventricle-here it is balanced dominance.
13

## Slide 65: Dominance
Right Dominance
Left Dominance
Co- Dominance

## Slide 66: Flow
TIMI grade:
  TIMI 0 flow (no perfusion) refers to the absence of any antegrade flow beyond a coronary occlusion.
  TIMI 1 flow (penetration without perfusion) is faint antegrade coronary flow beyond the occlusion, with incomplete filling of the distal coronary bed.
  TIMI 2 flow (partial reperfusion) is delayed or sluggish antegrade flow with complete filling of the distal territory.
  TIMI 3 is normal flow which fills the distal coronary bed completely

## Slide 67: Complications
Local:
  Bleeding
  Hematoma
  Infection
  Pseudoaneurysm
  Compartment Syndrome
Coronary
  Dissection, embolism, spasm

## Slide 68: Complications
Contrast related
  Contrast nephropathy
  Allergic reactions
  CHF
  Arrhythmias
Access vessel dissection
Stroke
Death

## Slide 69: Other coronary imaging modalities
CTA
MRA
IVUS
OCT (Optical Coherence Tomography)
Angioscopy