## Slide 1: Radiographic positioning of Upper Extremities
Yuvraj Maharshi
Lecturer
Department Of Paramedical Science,svdu

## Slide 2: Content
The upper Extremities consists of 60 bones:
Humerus - 2
Ulna - 2
Radius - 2
Carpals - 16
Metacarpals - 10
Phalanges - 28

## Slide 3: Humerus Anatomy
Longest and strongest bone of the upper limb.
The humerus articulates proximally at the shoulder joint .
The humerus articulates distally at the elbow joint.

## Slide 4: Indication of AP humerus
Exclude large humeral shaft fractures
Suspected symptomatic metastatic lesions
Trauma
Bony tenderness at the glenohumeral joint/region
Restriction of abduction
Suspected dislocation
Suspected bone tumors .

## Slide 5: AP Humerus
35 × 43 cm L.W. (14 × 17″)
Position:-Erect or supine with humerus aligned to long axis of IR Place shield over gonads.
Abduct arm slightly, supinate hand for true AP (epicondyles parallel to IR)
Central Ray: to mid humerus
Collimation:-

## Slide 6: Rotational Lateral Humerus
Erect (PA): Elbow flexed 90°, patient rotated 15°-20° from PA
Central Ray: mid humerus

## Slide 7: Trauma Lateral Humerus (Midhumerus and Distal Humerus)
30 × 35 cm L.W. (11 × 14″) or 24 × 30 cm L.W. (10 × 12″
No grid
Position:- Gently lift arm and place support block under arm, rotate hand into lateral position if possible for true lateral elbow projection.
Place IR vertically between arm and thorax with top of IR at axilla

## Slide 8: Trauma Transthoracic Lateral Humerus
35 × 43 cm L.W. (14 × 17″)
Grid
Position :- Patient lying down or erect
Affected limb closest to IR
Raise opposite arm over head
Central Ray : mid-shaft of affected humerus
Respiration:

## Slide 9: Forearm Anatomy
It consists of 2 bones :
Ulna
Radius
Proximal ends articulate with the humerus
Distal ends articulates with carpals

## Slide 10: Indication of forearm
Trauma
Bony tenderness
Suspected fracture
Obvious deformity
Non-traumatic pain
Suspected foreign body

## Slide 11: AP Forearm
35 × 43 cm L.W. (14 × 17″) or 30 × 35 cm (11 × 14″) for smaller patients
No grid
Position:-Patient seated at end of table with arm extended and hand supinated
Ensure that both wrist and elbow joints are included
Central Ray: midpoint of forearm

## Slide 12: Lateral Forearm
No grid
Position :- Elbow should be flexed 90°
Central Ray:- midpoint of forearm

## Slide 13: AP Elbow
24 × 30 cm L.W. (10 × 12″)
No grid
Position :- Elbow extended and hand supinated
Central Ray: mid elbow joint

## Slide 14: Lateral Elbow
24 × 30 cm L.W. (10 × 12″)
No grid
Position : elbow flexed at 90° ,shoulder dropped as needed to rest forearm and humerus flat on table and IR
Central Ray: mid elbow joint

## Slide 15: Trauma Axial Lateral Elbow (Coyle Method)
The Coyle's view is performed for any patient with a suspected radial head fracture 1-3 or dislocation.
Position and Central Ray : Elbow flexed 90° if possible,
Angle CR 45° toward thorax, centered to radial
head and neck (CR to enter at mid-elbow joint)

## Slide 16: Hand Anatomy
Carpals – 8
Wrist
She Looks Too Pretty Try To Catch
Her
S - scaphoid
L - lunate
T - triquetrum
P - pisiform
T - trapezium
T - trapezoid
C - capitate
H - hamate
Metacarpals -5
Palm
Head
Body
Base
Phalanges - 14 Fingers
Finger:- 4x3=12
Thumb:- 2
Proximal
Middle
Distal

## Slide 17: PA Hand
(10 × 12″)
18 × 24 cm L.W. (8 × 10″) smaller hand
No grid
Position :- Patient seated, hand on table, elbow flexed
Central Ray: Centered to 3rd MCP joint

## Slide 18: PA Oblique Hand
L.W.10 × 12 or 8 × 10
No grid
Position : Patient seated, hand on table, elbow flexed. Rotate entire hand and wrist laterally 45°, support with wedge or step block. Align hand and wrist to IR.
Central Ray: Centered to 3rd MCP joint

## Slide 19: “Fan” Lateral Hand
Anatomy : hand/wrist and 1″ (2.5 cm) distal forearm
interphalangeal and MCP joints open position
position : phalanges and metacarpal surfaces symmetric
distal radius, ulna, and metacarpals superimposed

## Slide 20: AP Oblique Bilateral Hand (Norgaard Method and Ball-Catcher’s)
10×12 crosswise or 14×17 crosswise
No grid
Position : Patient seated at end of table, both arms and hands extended with palms up and hands obliqued 45°, medial aspects touching.
Fingers fully extended supported by 45° support blocks.
Central Ray: CR ⊥, centered to midway between 5th MP joints

## Slide 21: Paediatric AP Upper Limb
IR size determined by
patient age and size
Position : Supine position, arm abducted away from body, lead shield over pelvic area
Include entire limb unless a specific joint or bone is indicated
Immobilize with clear flexible-type retention band and sandbags, or with tape
Use parental assistance only if necessary, provide lead gloves and apron
Central Ray: centered to mid limb