## Slide 1: Darkroom Illumination
Yuvraj Maharshi
Lecturer
Department Of Paramedical Science,svdu

## Slide 2
Place where necessary handling and processing of light sensitive film can be carried out safely and efficiently
Area from where a latent image is converted to a visible image
DAR
K
ROOM

## Slide 3: Darkroom illuminations
Ordinary white lighting
Safe lighting

## Slide 4: White lighting
Inspection and maintenance of cassettes and screens.
Cleaning of work surface and floors
Servicing of equipment.

## Slide 5
White lighting should be:
Close to ceiling.
Moderate in intensity(60W tungsten or 30W fluorescent)
Centrally placed

## Slide 6: Safe lighting
Dim, colored lighting which provides the sufficient illumination for handling, manipulating & processing the film.
A source of light - with no film fogging
- adequate illumination under
processing condition
Safe light is not totally safe

## Slide 7: Construction
Sheet of gelatin dyed filter sandwiched between two sheet of glass.
Fitted in metal lantern box.
Colored gelatin layer
Plain or clear glass
Diffusing glass
Color of the filter depends upon the sensitivity of
the x-ray film

## Slide 8: How dose safelight filters works???
The pigment in the filter selectively attenuates those parts of the spectrum to which the film is most sensitive.
Ultravoilet
Blue
Green
Red
Infra-red
Yellow light
Yellow Filter

## Slide 9: The pigment in the filter selectively attenuates those parts of the spectrum to which the film is most sensitive.
Ultravoilet
Blue
Green
Red
Infra-red
Red light
Red Filter

## Slide 10: Types
Direct safelighting :
- light from the safelamp
directly falls onto the
worksurface.
- e.g. beehive safelamp
- sited at distance of 1.2 m (4 ft)
- film loading and unloading areas

## Slide 11
Indirect safelighting :
- intended to provide
general illumination of dark
room.
- directs lamp towards the
ceilieng
- suspended 2.1 m above floor
level.

## Slide 12: Sensitivity of exposed and unexposed film
1- an increase in
gross fog
2- an overall loss
of contrast

## Slide 13: Safe film handling time
Tests to determine safe film handling time
Materials required:-
-Sheet of 30×35 cm card folded
and marked Sheet of 24х30 cm
card
- 24×30 cm screen -Type xray
film
- 24×30 cm xray cassette
- Densitometer

## Slide 14
50
40
30
20
10
60
A folded card film holder for carrying out a safe film-handling time test

## Slide 15: PROCEDURE
Load the cassette – no safelight is used
In the x ray room mask one half of the cassette lengthwise with a peace of lead
Make an exposure

## Slide 16
A
B
C
D
3 MIN 30 SEC
2 MIN 30 SEC
1 MIN 40 SEC
1 MIN
30 SEC
10 SEC
X RAY
XRAY
+SAFELIGHT
Only SAFELIGHT
No safelight no xray
LEAD
while exposing

## Slide 17
In the darkroom unload the film and place in the cardboard holder
Place the second sheet of card on top
Switch on the safelight to be tested

## Slide 18
A
B
C
D
3 MIN 30 SEC
2 MIN 30 SEC
1 MIN 40 SEC
1 MIN
30 SEC
10 SEC
X RAY
XRAY
+SAFELIGHT
Only SAFELIGHT
No safelight no xray
60
10 s
20s
30s
40s
50s
60s
60
10 s
20s
30s
40s
50s
CARDBOARD
AFTER XRAY EXPOSURE
EXPOSURE TO SAFE LIGHT

## Slide 19
Move the covering card down to the first marked line and expose the uncovered portion of the film for 1 min
The card is then moved to the next uncovered portion and expose for 50 sec
Proceed in the same way until the entire film has been exposed
Turn off the safelight and process the film

## Slide 20
A
B
C
D
3 MIN 30 SEC
2 MIN 30 SEC
1 MIN 40 SEC
1 MIN
30 SEC
10 SEC
X RAY
XRAY
+SAFELIGHT
Only SAFELIGHT
No safelight no xray
60
10 s
20s
30s
40s
50s
60s
60
10 s
20s
30s
40s
50s
CARDBOARD
exposure to safe light

## Slide 21
D’ | D’+0.05 Safe time to handle exposed film | D+0.05 Safe time to handle unexposed film | 
A
B
C
D
3 MIN 30 SEC
2 MIN 30 SEC
1 MIN 40 SEC
1 MIN
30 SEC
10 SEC
X RAY
XRAY
+SAFELIGHT
Only SAFELIGHT
No safelight no xray
D
After processing-calculating value with densitometer
Safe light handling time ranges b/w 20 – 45 sec

## Slide 22: when should the test be carried out?
New darkroom
Where safelights have been changed or additional safelights added
If faster film material is introduced into a department
Whenever it is suspected that safelight fogging is occurring
Quality assurance programme